## Slide 1
Node and link failure detection
Stefano Maxenti 10526141
Marco Bottenghi 10800598
Elisabetta Cainazzo 10800059
Switching and Routing - project 2020/2021
Prof. Guido Maier, Achille Pattavina
Tutor Sebastian Troìa

## Slide 2: Outline
Introduction
Reactive approach
Proactive approach
Link Removal algorithm
Link addition algorithm
Mininet Results
Real implementation results
Conclusion and future work

## Slide 3: Introduction
We have developed two version of the RYU controller: reactive and proactive
Creation of specific function for path discovery and rules installation
Well-known problem in OpenFlow, the rule installation is not atomic
The solution is the Barrier message, used to force the switch to suspend all activities until the rules are installed
The disadvantage is that the internal switch optimization may be bypassed, this involves a bit slower installation

## Slide 4: Reactive approach and Proactive approach
Listen to OpenFlow messages sent by the switches to the controller and react accordin-gly
Activation of a RYU controller any time there is an event
link_ del_handler_reactive is the main trigger function, it creates a thread for each one of the failed link, to avoid halts due to switch abruptly disconnected
Threads allows to parallelize work and overcomes the waiting
Check the link status every t seconds, to find out whether a link has been disconnected
We memorize link status in a list, and confront this list with the previously memorized one
Creation of a thread for each link to be removed to avoid the halting of the system
Installation of main and back-up rule with lower priority to reduce delay
Restoration of the shortest path after recovery

## Slide 5: Link removal and addition algorithm
Started from the template but modified this function
React to the message that an-nounces that a link has been added
Update the topology in the reactive, while on the proactive we also restore the shortest path for all rules
Starting from the rules reque-sted from the Data-paths, we send a delete request to all switches
Separate function created for path calculation and rules installation comes in handy
Extract link information from input parameter and check that it is present
If the link is present, ask to Datapath. This permit to reset only the rule that inclu-de the failed link
Remove the link from the graph
Starting from the rules re-quested from the Datapaths, we send a delete request to all switches
Verify that all switches are still available
If switch is disappeared, we remove it

## Slide 6: Mininet results
We test with the following tools:
  Ping between pairs of hosts while removing links and turning off switches
  Long iperf3 connections between hosts while removing links and turning off switches
  D-ITG test to verify the number of lost datagrams while removing links and turning off switches

## Slide 7: Mininet results
Reactive approach
Command pingall to verify that each host can communicate with each other by installing the correct flow
Starting a terminal with a ping between two hosts. Then we remove a link and observe that the traffic is correctly rerouted on the opposite flow
Trying with iperf3: flows are correctly rerouted in the opposite direction
Proactive approach
Two rules installation for each flow, primary and secondary rule (longer)
The delay is compensated when the network reacts to the failure, takes less than a second
Backup rule is already installed, no extra-time is spent finding a path
Automatically restore to the shortest path

## Slide 8: Mininet results: extra
Bigger topology: 18 switches with one host each. As before, a pingall command shows reachability between each one of the 306 combinations of hosts.

## Slide 9: Mininet results: extra
Bigger topology with more hosts: adding ports we can try if it works in the case there are more than one hosts per switch. We can try this only in Mininet. All works correctly.
Crossed topology: our code is immediately extensible to a crossed topology. Implementation work correctly and flows are recovered immediately.

## Slide 10: Real implementation results
Link removal and addition worked, node failure was very tricky
Pulling the electrical plug from a switch doesn’t allow it to communicate to the controller that it is being shut down
In the first version, the removal of a switch would halt the program, the controller didn’t realize that the switch was off
To manage it we don’t use RYU functions, but implemented our owns
In Lab everything is a bit slower. Notification time is better in reactive mode, but reaction time is faster in proactive, since there is no need to calculate anything.
Values were, in any case, under 2 seconds.

## Slide 11: Conclusion
We tried to write an easily extensible code, tested in Mininet (the topology is not relevant)
Creating small functions makes it easy to use a black-box approach that could be useful in the future
Both implementations have pros and cons and the choice must consider the specific traffic scenario
Hybrid approach might be a viable solution, even though it duplicates function and increase the complexity of the solution
Further testing may be needed before being put into production

## Slide 12: Future work
Even though the deletion rule is quite fast, we send the message to delete the specific to all switches. An even better algorithm could filter out the switches that don’t contain it
Using OpenFlow 1.4 or higher and the BundleMsg option instead of Barrier would be faster and more optimized. However, not only Ryu has to be updated, but also the switches (Zodiac FX switches in lab may not be compatible)
More powerful hardware could be used, for example routers with OpenWRT and the OpenFlow packages.

## Slide 13
THE END
Questions?